## Slide 1: draft-kampanakis-tls-scas-latest-00 (was draft-thomson-tls-sic) https://github.com/csosto-pk/tls-suppress-intermediates
Martin (Mozilla)
Panos (AWS)
Cameron (AWS)
Bas (Cloudflare)

## Slide 2: Problem: TLS is heavy in auth data
TLS includes a few Sigs & PKs
  (x+1) Sigs + (x+1) Public Keys, where x is the # of ICAs in the chain
  1 CertificateVerify signature
  2+ SCT signatures (WebPKI)
  1 OCSP signature (sometimes)
Issues
  Post-quantum Signature and Public Key sizes
    can lead to 10+ KB auth data size increases
    will introduce at least one round-trip in QUIC
  draft-ietf-emu-eaptlscert and draft-ietf-emu-eap-tls13
  Wi-SUN Field Area Networks, IEEE 802.15.4 mesh networks
Notes: draft-ietf-emu-eap-tls13
Including ContentType (1 byte), ProtocolVersion (2 bytes), and length (2 bytes) headers a single TLS record may be up to 16645 octets in length. EAP-TLS fragmentation support is provided through addition of a flags octet within the EAP-Response and EAP-Request packets, as well as a (conditional) TLS Message Length field of four octets. Implementations MUST NOT set the L bit in unfragmented messages, but MUST accept unfragmented messages with and without the L bit set. Some EAP implementations and access networks may limit the number of EAP packet exchanges that can be handled. To avoid fragmentation, it is RECOMMENDED to keep the sizes of EAP-TLS peer, EAP-TLS server, and trust anchor certificates small and the length of the certificate chains short. In addition, it is RECOMMENDED to use mechanisms that reduce the sizes of Certificate messages. For a detailed discussion on reducing message sizes to prevent fragmentation, see [I-D.ietf-emu-eaptlscert].
draft-ietf-emu-eaptlscert
Unlike the use of TLS on the web, where typically only the TLS server is authenticated; EAP-TLS deployments typically authenticate both the EAP peer and the EAP server. Also, from deployment experience, EAP peers typically have longer certificate chains than servers. This is because EAP peers often follow organizational hierarchies and tend to have many intermediate certificates. Thus, EAP-TLS authentication usually involves exchange of
Section 3.1 of [RFC3748] states that EAP implementations can assume a Maximum Transmission Unit (MTU) of at least 1020 octets from lower layers. The EAP fragment size in typical deployments is just 1020 - 1500 octets (since the maximum Ethernet frame size is ~ 1500 bytes). Thus, EAP-TLS authentication needs to be fragmented into many smaller packets for transportation over the lower layers. Such fragmentation not only can negatively affect the latency, but also results in other challenges. For example, some EAP authenticator (access point) implementations will drop an EAP session if it has not finished after 40 - 50 round-trips. This is a major problem and means that in many situations, the EAP peer cannot perform network access authentication even though both the sides have valid credentials for successful authentication and key derivation.

## Slide 3: Big certificate chains slow down TLS
ia.cr/2020/071, dl.acm.org/doi/10.1145/3386367.3431305 show that
  cert chains exceeding TCP initcwnd slow down the handshake (round-trips)
ia.cr/2019/1447 shows that
  Big certificate chains (even smaller than the TCP initcwnd) slow down the handshake in lossy conditions.
Cloudflare Blog shows that >9-10KB cert chains (even with 30MSS initcwnd) leads to double digit slowdown

## Slide 4: PQ TLS authentication data (in KB)
 | 1 ICA | 2 ICAs | 3 ICAs | NIST PQ Signature
TLS (no SCTs, no OCSP staples) | 8.77 | 11.94 | 15.12 | Dilithium-2
 | 3.76 | 5.31 | 6.86 | Falcon-512
 | 89.12 | 133.64 | 178.16 | Rainbow-I(cz)
 | 20.44 | 26.73 | 33.02 | SPHINCS+-128s
Web (SCTs, no OCSP staples) | 12.40 | 15.57 | 18.75 | Dilithium-2
 | 4.76 | 6.31 | 7.85 | Falcon-512
 | 89.21 | 133.74 | 178.26 | Rainbow-I(cz)
 | 32.22 | 38.51 | 44.80 | SPHINCS+-128s
Web (SCTs, OCSP staples) | 14.82 | 17.99 | 21.17 | Dilithium-2
 | 5.43 | 6.97 | 8.52 | Falcon-512
 | 89.28 | 133.80 | 178.33 | Rainbow-I(cz)
 | 40.08 | 46.37 | 52.66 | SPHINCS+-128s

## Slide 5: ICA suppression in TLS 1.3
Pre-acquire a “fresh” (TBD3-time) ICAs list and
Ask the peer to not send ICAs by using tlsflag TBD1 in
  ClientHello (server auth)
  CertificateRequest (mutual auth)
Why
  TLS (including Web) PQ auth data stay within acceptable levels
    Saves ~3.2 / 1.6 KB for 1 ICA with NIST Round 3’s two leanest PQ Sig finalists
    Saves ~6.4 / 3.1 KB for 2 ICAs with NIST Round 3’s two leanest PQ Sig finalists
  Low hanging fruit

## Slide 6: PQ TLS authentication data w/o ICAs (in KB)
 | 1 ICA | 2 ICAs | 3 ICAs | NIST PQ Signature
TLS (no SCTs, no OCSP staples) | 5.59 | 5.59 | 5.59 | Dilithium-2
 | 2.21 | 2.21 | 2.21 | Falcon-512
 | 44.59 | 44.59 | 44.59 | Rainbow-I(cz)
 | 14.15 | 14.15 | 14.15 | SPHINCS+-128s
Web (SCTs, no OCSP staples) | 9.22 | 9.22 | 9.22 | Dilithium-2
 | 3.21 | 3.21 | 3.21 | Falcon-512
 | 44.69 | 44.69 | 44.69 | Rainbow-I(cz)
 | 25.93 | 25.93 | 25.93 | SPHINCS+-128s
Web (SCTs, OCSP staples) | 11.04 | 11.04 | 11.04 | Dilithium-2
 | 3.71 | 3.71 | 3.71 | Falcon-512
 | 44.74 | 44.74 | 44.74 | Rainbow-I(cz)
 | 31.82 | 31.82 | 31.82 | SPHINCS+-128s

## Slide 7: About ICA lists
WebPKI: Total <1,500 ICAs / ~1-2 MBs compressed
In some (non WebPKI) usecases, the ICA list can be built dynamically.
Send ICAs regardless of tlsflag to prevent failures, if your ICAs are not
  published (constrained) (MSRP 2.8 may change that)
  in the list hosted by a public repo (e.g. CCADB)
Similar Precedents
  Mozilla already uses an ICA Pre-load list
  Browsers build and distribute revocation lists
  draft-ietf-tls-ctls defines a compression certificate dictionary
Notes: Mozilla Root Store Policy (MSRP) https://www.mozilla.org/en-US/about/governance/policies/security-group/certs/policy/
MSRP 2.8 may require constrained intermediates, so we may not need to send Constrained ICAs.
Additional bullet scenario for second bullet
Send ICAs regardless of tlsflag, if your
  ICAs may not exist in the peer ICA list (e.g. private PKI ICA change)

## Slide 8: Open Questions
What is the recommended TBD3-time?
Who maintains the list of ICAs?
  Client / browser vendor
  CCADB or other public repo.
What if there is a failure
  Connection re-try and its impact on security and privacy
    Could the fallback logic allows for downgrade style of attacks?
    Active attack analysis.
or can we assume no failure?

## Slide 9: Closing Comment & Asks
Challenges for WebPKI
  We believe addressing them is possible
  But also, let’s not forget, TLS is not just for the Web
Discussion on the draft in the WG or git repo
https://github.com/csosto-pk/tls-suppress-intermediates
Consider it for WG adoption after NIST announces its Round 3 picks.
Notes: We could push this draft as Experimental so it is not mandatory for WebPKI.